## Slide 1: Design of Cane Juice Evaporator

## Slide 2: Calandria Evaporator

## Slide 3: Heat Transfer Coefficient
Dessin’s Model
  U depends heavily on brix and steam temperature

## Slide 4: Evaporator Construction
Too high evaporator gives too much heat loss
Too short evaporator gives bad separation between liquid and vapor.
Design Guideline
The height of calandria body above calandria should be 1.5 – 2 the length of the tube

## Slide 5: Evaporator Diameter
The diameter of evporator has an important effect on entrainment.
Area of horizontal cross section should provide 1m2/400 m3/h of vapor produced.
The velocity of vapor leaving the liquid surface should not be higher than 4.6 m/s

## Slide 6: Center Wall
Center wall is utilized to collect the concentrated juice in order to remove it from one evaporator to the next calandria.
The diameter of center wall varies from ¼ to 1/8 of the vessel diameter.

## Slide 7: The tube
The commonly used stainless steel tube is 35.6 mm ID and 38.1 mm OD.
Recommended tube length
Recommended Tube Length of the Multiple Effect |  |  |  | 
1st vessel | 2nd vessel | 3rd vessel | 4th vessel | 5th vessel
4 m | 3.5 m | 3 m | 2.5 m | 2.25 m

## Slide 8: Arrangement of the Tubes
Staggered Arrangement

## Slide 9: Lab
ให้ออกแบบ Evaporator สำหรับโรงงานน้ำตาลที่กำหนดให้ครบทุก Evaporator
  ขนาดท่อ
  จำนวนและความยาวท่อ
  ขนาดของ Tube Sheet (diameter)
    วิเคราะห์จากพื้นที่ที่วางท่อได้ตามจำนวน
  ขนาดของ Center Wall
  ความหนาของผนัง Evaporator (จากการวิเคราะห์ความเค้น)
  อาจปรับขนาดของ Evaporator ให้เป็นหลายชุดขนานกันได้
  เช็คความเร็วของไอหัวหม้อที่ออกจากผิวน้ำอ้อยด้วย

## Slide 10: Typical Cane Juice Heater

## Slide 11: Typical Evaporator