## Slide 1: VIRTUAL REALITY (ความเป็นจริงเสมือน)
Pitipong Pimpiset

## Slide 2: Lecture 0 Motion CAPTURE
VIRTUAL REALITY

## Slide 3: Watch this !
Final Fantasy spirits within

## Slide 4: Motion Capture

## Slide 5: What is Motion Capture?
Motion Capture
is the specific way to capture motion of (human) actor such as,
  Whole body
  Upper body
  Face

## Slide 6: More generally…
Motion Capture or Mocap is the process of recording the movement of objects or people. It is used in various industries like entertainment (film making, game), sports or medical applications.

## Slide 7: History of Mocap
The idea of copying human motion for animated characters is not new. In the late 1970’s, Disney’s Snow White was the first movie that traced animation over film footage of live actors playing out the scenes. This method, called “rotoscoping” has been successfully used for human characters ever since. For more in-depth information
http://www.siggraph.org/education/materials/HyperGraph/animation/character_animation/motion_capture/history1.htm

## Slide 8: Principle
Capture movements or postures in the real world
  actor (body, hands, face)
  puppet (body)
Extract relevant data
Use data
  Map the movements to a synthetic creature
  Execute commands

## Slide 9: How it works
This workflow based on the Mocap system from Motion Analysis http://www.motionanalysis.com/
Set up the system (Camera, performing area)
Calibrate the system (avoid any reflectable surface, light source)
Create template for any motion
Clean up the captured data and save as a useable format
Start mocaping !

## Slide 10: Then…
Import it to Motion Builder
Import your character and make some adjustment to both data and character
Finally you will get the lively character !
http://www.youtube.com/watch?v=1wK1Ixr-UmM

## Slide 11: Types of Mocap
Magnetic
Mechanical
Optical

## Slide 12: Magnetic

## Slide 13: How it works?
Source and sensors
  emit and receive magnetic fields
Electronic control unit
  computes positions and orientations
Server/driver
  sends the data to the computer(s)
  one channel/sensor
Tracks (one/variable)

## Slide 14: Magnetic
This approach has a central magnet with several receivers attached to the actor’s body. The receivers capture and record the actors movements and save them to the computer. This motion capture method can be hindered by nearby metal objects if they are large enough and depending on the power of magnets being used.

## Slide 15: Advantages & Disadvantages
Position and orientation
Minimal device calibration
Real-time
Cheap ($40000)
Limited range
  10-15 m2
Sensitivity to metal
Encumbrance
Sampling rate
Advantages
Disadvantages

## Slide 16: Mechanical Motion Capture

## Slide 17: Mechanical Motion Capture
Subject wears an exoskeleton
No interference from light or magnetic field
No marker confusions
No range limit
Some restriction of movement
Absolute position is unknown

## Slide 18: Optical
Use retro-reflective markers
  circular stickers
  small spheres
Cameras
  facial animation: 1
  body animation: 2-6
Postprocessing of images

## Slide 19: Optical body tracking: practice
20-30 markers
  Points of interest
  hips, elbows, knees,...
  head (3 markers)
Images are postprocessed (tracking)

## Slide 20: Advantages & Disadvantages
Large active area
Unemcumbered actor
Markers are passive
High enough sampling rates
Cost ($150,00 - 250,000)
Sensitivity to light
Sensitivity to reflections
Marker occlusions
Tracking time
Positions only
Sensitivity to calibration
Advantages
Disadvantages

## Slide 21
Production Pipeline of Motion Capture
Sensor Calibration
Subject Calibration
Record Movements
Compute the position and orientation of camera/transmitter
Place markers on body, compute skeleton structure(lengths of links)
Marker positions (and orientations) varying over time
Marker Data Cleanup
Convert to Joint Angles
Occlusion and correspondence problems
Occlusion and correspondence problems
Mapping to characters
Direct Mapping or retargetting

## Slide 22: Sources of errors
Magnetic sensors
Calibration
Trackers not rigidly fixed

## Slide 23: So… what if you want to play with Mocap
http://www.youtube.com/watch?v=p2qlHoxPioM
http://www.youtube.com/watch?v=pPt_944t9Lcb
http://www.youtube.com/watch?v=pEreBbkL3fU

## Slide 24: References
www.siggraph.org
www.motioncapturesociety.com
www.motion-capture-system.com

## Slide 25: Activity
Today’s activity…
  Watch a provided video about Mocap and make a summarize about it.
  What do think of this technology? Does it help us to create animation easier?
  If you are able to use this technology to create something, what will you do?